## Slide 1: Gonioscopy and Glaucoma
A Self-Assessment Module by the American Board of Optometry

## Slide 2: Gonioscopy: A Primer
Types of lenses
Landmarks
Performing the procedure
Recording the results
Billing for the procedure

## Slide 3: Anatomic Structures Visible Using Gonioscopy
Schwalbe’s Line
Trabecular meshwork
  - Pigmented
  - Non- pigmented
Scleral spur
Ciliary body band
Peripheral iris

## Slide 4: A Look into the Angle
Modified from a figure by T.Tarrant. Simon Barnard, City University London

## Slide 5: Total Internal Reflection
Angle cannot be viewed with external light source alone because of total internal reflection
  Curvature of cornea
  Index of refraction for air is different than for optical tissue
Contact lens needed to eliminate the air to cornea interface, enabling a view of the angle

## Slide 6: Gonioscopic Lenses: Goldmann Lens

## Slide 7: Gonioscopic Lenses: Zeiss Lens

## Slide 8: Other Zeiss Type Gonioscopic Lenses: Posner Lens

## Slide 9: Other Zeiss Type Gonioscopic Lenses: Sussman (same as Zeiss or Posner but without the handle)

## Slide 10: Gonioscopic Technique: Advantages of Zeiss/Posner/Sussman Lenses
Topical anesthesia
No coupling agent
Lens stays stationary
Move slit lamp to view all quadrants
Eye gaze direction ─ toward viewing mirror to see deeper into angle

## Slide 11: Gonioscopic Technique Tip Start with superior and inferior mirrors for the easiest view. For nasal and temporal mirrors, move slit lamp light housing opposite to the mirror you are looking into, and shine light directly in.

## Slide 12: Gonioscopic Technique: Zeiss/Posner/Sussman Lenses
Pros
  Done with topical proparacaine, following applanation tonometry
  Can perform indentation gonioscopy in the case of chronic or acute angle closure
  Central mirror can be used as a fundus lens
Cons
  A slight learning curve
  Air bubble can obscure view
  Possible to push lens too hard against cornea
  Folds in Descemet’s are an indicator to back off

## Slide 13: If cooperation is a problem:
Try a drop of Lidocaine 3.5% gel (Akten by Akorn)
Deeper anesthesia can make for an easier exam

## Slide 14: Angle Classification Systems

## Slide 15: Angle Classification Systems
Shaffer
  Based on angular width of recess
  Grade 0 (partly/totally closed) to grade 4 (30-45)
Scheie
  Based on extent of angle structures visualized
  Wide open (Grade I) to occluded (Grade 4) [reverse of current grading systems]
Spaeth
  Based on angular approach to recess, configuration of peripheral iris, insertion of iris root
  A (anterior to Schwalbe’s line) through E (extremely deep); grades A and B are always pathological

## Slide 16: Recording Your Findings Using the Shaffer System (most commonly used)
Grading system IV (wide open), III, II, I, slit, closed
Grid drawing
Label each quadrant numerically or with description of structures seen (i.e., CBB, or 2+ PTM), preferably both!
If angle is the same 360, make things simple and record as follows. (See next slide)

## Slide 17
IV CBB 360

## Slide 18: Recording Gonioscopy: More Examples
IV CBB
A. Recess
III SS
II TM
CBB Ciliary Body Band
SS Scleral Spur
TM Trabecular mesh

## Slide 19: Gonioscopy Guidelines
Baseline gonioscopic exam for every:
  New glaucoma suspect
  Already diagnosed glaucoma patient
  Pt with family history of glaucoma
  Pt with shallow chambers
  Pt with history of transient pain, blurred vision

## Slide 20: Gonioscopy Guidelines
Repeat if neovascularization or sudden change in pressure
Repeat yearly:
  Post-iridotomy
  If angle shows narrowing
Repeat yearly:
  Open angle (COAG) patients
  Hyperopes older than 40 years
van Herick angle of grade 2 or less*
*AOA Practice Guidelines

## Slide 21: Billing
Gonioscopy is a billable procedure
Code 92020
Use a 92 or 99 code (E/M) exam code along with separate gonioscopy charge